## Slide 1: Campus Fabric Demo using mist
Mochammad Irzan

## Slide 2
Objective:
To demo on how to use MIST to configure campus fabric infrastructure (ip Clos)

## Slide 3: Topology
Desktop1
Desktop2
Access1
AP1
Desktop3
Desktop4
Access2
AP2
Desktop5
Desktop6
Access3
AP3
Desktop7
Deskto8
Access4
AP4
Firewall
External
kvm
Core1
Core2
vm1
vm2
vm3
DHCP server, Radius Server
virtualJunos
dist1
dist2
ge-0/0/2
ge-0/0/3
ge-0/0/2
ge-0/0/3
ge-0/0/2
ge-0/0/3
ge-0/0/2
ge-0/0/3

## Slide 4: Connectivity
Device A | Port on Dev. A | Port on Dev. B | Device Z
core1 | ge-0/0/0 | ge-0/0/1 | firewall
core2 | ge-0/0/0 | ge-0/0/2 | firewall
core1 | ge-0/0/1 | ge-0/0/0 | dist1
core1 | ge-0/0/2 | ge-0/0/0 | dist2
core2 | ge-0/0/1 | ge-0/0/1 | dist1
core2 | ge-0/0/2 | ge-0/0/1 | dist2
core1 | ge-0/0/7 | eth1 | kvm
core2 | ge-0/0/7 | eth2 | kvm

## Slide 5: Connectivity
Device A | Port on Dev. A | Port on Dev. B | Device Z
dist1 | ge-0/0/2 | ge-0/0/0 | access1
dist1 | ge-0/0/3 | ge-0/0/0 | access2
dist1 | ge-0/0/4 | ge-0/0/0 | access3
dist1 | ge-0/0/5 | ge-0/0/0 | access4
Device A | Port on Dev. A | Port on Dev. B | Device Z
dist2 | ge-0/0/2 | ge-0/0/1 | access1
dist2 | ge-0/0/3 | ge-0/0/1 | access2
dist2 | ge-0/0/4 | ge-0/0/1 | access3
dist2 | ge-0/0/5 | ge-0/0/1 | access4

## Slide 6: Mist configuration
Create Organization, Site, and template, and assign site to template
Adopt switches
Create campus fabric, IP Clos
Connect wired client
Connect external gateway/firewall
Change management network to inband
Connect server : DHCP Server, Radius Server
Configure DHCP relay for client, configure 802.1X authentication
Configure dynamic port configuration

## Slide 7: Organization, site and template
Create organization
  Name : demo1
Create site
  Site name: campus1
  Location: Jakarta
  Timezone: Asia/Jakarta
Create template
  NTP server: anyntp.juniper.net
  DNS server: 10.49.32.95, 10.49.32.97
  Root password: pass01
Assign Template to site

## Slide 8: Adopt Switches into Mist
Verify that the switches are able to access internet
Adopt Switches
Assign switches to Site
Enable MIST to manage the switches

## Slide 9: Create campus Fabric
Create campus fabric, IP Clos
Add the switches into the campus fabric
Create two network and add them into one VRF
Deploy campus fabric
Verify that campus fabric is deployed
network | vlan | subnet | Gateway | VRF
vlan101 | 101 | 192.168.101.0/24 | 192.168.101.1 | RZ1
vlan102 | 102 | 192.168.102.0/24 | 192.168.102.1 | RZ1

## Slide 10: Connect Wired Client
Create port profiles for network vlan101 and vlan102
Configure port using port profile created on previous step
Configure static ip address on wired client and test connectivity
Switch | port | Wired client | vlan
access1 | ge-0/0/2 | desktop1 | 101
 | ge-0/0/3 | desktop2 | 102
access2 | ge-0/0/2 | desktop3 | 102
 | ge-0/0/3 | desktop4 | 101
access3 | ge-0/0/2 | desktop5 | 
 | ge-0/0/3 | desktop6 | 
access4 | ge-0/0/2 | desktop7 | 
 | ge-0/0/3 | desktop8 | 

## Slide 11: Enabling Symmetric IRB with EVPN type 2
Set additional CLI commands on access switches
  set routing-instances <VRF> protocols evpn irb-symmetric-routing vni <vni_id>

## Slide 12: Connecting to external gateway for VRF
Device | Interface | vlan | ip address | VRF | Routing
core1 | ge-0/0/0 | 301 | 192.168.31.1/31 | RZ1 | BGP
core2 | ge-0/0/0 | 301 | 192.168.31.3/31 | RZ1 | BGP
Device | ASN
External gateway | 65412
core1/core2 | 65420

## Slide 13: Connecting to external gateway for underlay
Device | Interface | vlan | ip address | Routing
core1 | ge-0/0/0 | 1001 | 172.16.101.1/31 | Static
core2 | ge-0/0/0 | 1001 | 172.16.101.3/31 | static
network | vlan | subnet | gateway
vlan1002 | 1002 | 172.16.102.0/24 | 172.16.102.1
Device | vlan | ip address on IRB | Routing
access1 | 1002 | 172.16.102.11/24 | Static
access2 | 1002 | 172.16.102.12/24 | Static
access3 | 1002 | 172.16.102.13/24 | Static
access4 | 1002 | 172.16.102.14/24 | Static

## Slide 14: Setting routing for underlay
Set ip configuration (out of band) to static
Set default route on distribution switch
  set routing-options static route 0.0.0.0/0 next-hop <IP loopback of core1> resolve
  set routing-options static route 0.0.0.0/0 next-hop <IP loopback of core2> resolve
Set default route on access switch
  set routing-options static route 0.0.0.0/0 next-hop <IP loopback of dist1> resolve
  set routing-options static route 0.0.0.0/0 next-hop <IP loopback of dist2> resolve

## Slide 15: Create another VRF
Device | Interface | vlan | ip address | VRF | Routing
core1 | ge-0/0/0 | 302 | 192.168.31.5/31 | RZ2 | BGP
core2 | ge-0/0/0 | 302 | 192.168.31.7/31 | RZ2 | BGP
network | vlan | subnet | Gateway | VRF
vlan201 | 201 | 192.168.201.0/24 | 192.168.201.1 | RZ2
vlan202 | 202 | 192.168.202.0/24 | 192.168.202.1 | RZ2

## Slide 16: Configure DHCP server and Radius Server
Device | Interface | vlan | ip address | VRF
core1 | ge-0/0/7 | 401 | 192.168.41.1/24 | RZ1
core2 | ge-0/0/7 | 401 | 192.168.41.1/24 | RZ1
Device | Interface | vlan | ip address | VRF
core1 | ge-0/0/7 | 501 | 192.168.51.1/24 | RZ2
core2 | ge-0/0/7 | 501 | 192.168.51.1/24 | RZ2
Device | Interface | vlan | ip address | VRF
core1 | ge-0/0/7 | 1002 | 172.16.102.1/24 | underlay
core2 | ge-0/0/7 | 1002 | 172.16.102.1/24 | underlay
DHCP server for VRF RZ1
DHCP server for VRF RZ2
RADIUS server for VRF RZ1

## Slide 17: Enabled DHCP and 802.1X
Enable DHCP relay for dhcp client
Enable 802.1X authentication

## Slide 18: Configure dynamic port configuration
Configure dynamic port configuration based on LLDP information of the wired client